## Slide 1
RESULTS AND CONCLUSIONS
The initial exploratory findings demonstrate that the BME688 environmental sensor can reliably differentiate between waste materials and normal air through their VOC signatures. Normal air exhibits moderate negative correlations between resistance and temperature and between temperature and humidity. The resistance measurements indicate that ash produces the lowest and most uniform readings, coffee shows more variable results including several extreme spikes, and clean air exhibits the highest readings with the widest spread.
These findings confirm the BME688's capacity to distinguish between ash, coffee, and air, supporting its use in intelligent waste monitoring applications.
In conclusion, this research presents the initial phase of an intelligent waste management system that can detect hazardous materials, optimize collection routes, and provide valuable data insights.
The findings support the development of a system that can monitor waste conditions in real-time and enhance environmental and economic benefits. Future research will focus on field-testing the sensor units in real waste containers, developing more sophisticated classi-fication algorithms, and integrating the sensor subsystem with route optimization and data analysis platforms.
METHODOLOGY
BACKGROUND
OBJECTIVES
Urban waste management constitutes a critical infrastructure challenge for modern cities. Traditional waste collection methodologies operate on fixed schedules regardless of actual container fill levels, resulting in inefficient resource allocation, unnecessary carbon emissions, and occasional overflow incidents. Additionally, the inability to detect hazardous materials creates environmental and safety risks, particularly with improperly disposed hot ash that can cause fires in waste containers [1]. Smart sensors, artificial intelligence, and optimization algorithms offer a transformative approach to monitor waste conditions in real-time and provide actionable insights to stakeholders [2].
The Bosch BME688 environmental sensor was selected for its ability to simultaneously measure gas concentration, temperature, humidity, and pressure in a compact and energy-efficient format [2]. The experimental setup connected the BME688 development kit to a microcontroller for continuous data acquisition.
The sensor was chosen because of its ability to detect volatile organic compounds and monitor environmental conditions in waste samples. Measurements were carried out on controlled samples of coffee grounds and ash, interspersed with readings in ambient air.
This approach establishes a reliable baseline and minimizes the risk of cross-contamination, making it possible to clearly distinguish between environmental
variations and the specific signatures of residues. The sensor was first calibrated in clean air, then each material was exposed in sealed conditions for 30 minutes, resulting in approximately 1000 cycles per sample, with a clean air baseline wash before the first exposure and after each sample.
Throughout each exposure, gas resistance, temperature, humidity, and pressure were recorded at regular intervals. This cycle of sample exposure, baseline wash, and subsequent sample ensures clear, interference-free signatures for each material, supporting the development
of a more sustainable and efficient urban waste infrastructure.
Evaluate BME688 sensor suitability - for monitoring volatile organic compounds (VOCs) in organic waste containers to determine chemical signature detection capabilities.
Differentiate waste types through chemical signatures - using controlled samples of coffee grounds and ash with normal air readings to establish baseline measurements.
Develop real-time monitoring capabilities - to detect potentially dangerous materials in waste streams and enhance worker safety.
Establish foundation for smart waste system - integrating sensor technology with artificial intelligence and optimization algorithms for comprehensive waste management.
Optimize collection efficiency - to reduce collection frequency, lower fuel consumption, and decrease carbon emissions through data-driven insights.
BIBLIOGRAPHY
Kaza, S., Yao, L., Bhada-Tata, P., & Van Woerden, F. (2018). What a waste 2.0: a global snapshot of solid waste management to 2050. World Bank Publications.
Bosch Sensortec. BME688 Environmental Sensor Technical Documentation. Available at: [Bosch Sensortec Official Documentation]
VOC Pattern Recognition in Waste Using AI-Enabled BME688 Sensors
Felipe Merenda Izidorio, Mariam Jvarsheishvili, Getúlio Igrejas, Pedro João Rodrigues, Rui Pedro Lopes
felipeizidorio@ipb.pt , mariam@ipb.pt
Research Center in Digitalization and Intelligent Robotics (CeDRI), Laboratorio Associado para a Sustentabilidade e Tecnologia em Regioes de Montanha (SusTEC)
Acknowledgements: The authors are grateful to the Foundation for Science and Technology (FCT, Portugal) for financial support through national funds FCT/MCTES (PIDDAC) to CeDRI, UIDB/05757/2020 (DOI: 10.54499/UIDB/05757/2020) and UIDP/05757/2020 (DOI: 10.54499/UIDP/05757/2020) and SusTEC, LA/P/0007/2020 (DOI: 10.54499/LA/P/0007/2020).
Figure 1. Boxplot of Resistance Gas Sensor by Condition